Designer: Choose the size of maintainable drain, add proper source code.  Add/Remove/Edit options shown in red as listed below according to project specific needs.  Once that is done, ensure there is no remaining red text and delete this note.  Submit for review and approval.

MICHIGAN

DEPARTMENT OF TRANSPORTATION

SPECIAL PROVISION

FOR

MAINTAINABLE DRAIN, STEEL

Source Code	1 of 2	APPR:DMG:RWS:11-01-19

a.	Description.  This work consists of furnishing and installing a weep hole maintainable drain filter assembly, including all necessary hardware at the location(s) shown on the plans.  This item includes all work required to core drill a weep hole in the existing [INSERT PROJECT SPECIFIC STRUCTURE SUCH AS RETAINING WALL, ABUTMENT WALL, SHEET PILE WALL], and install the maintainable drain filter assembly.  Ensure all work and materials are in accordance with the standard specifications, except as modified herein.

b.	Materials.  Provide drain filter housings fabricated from [stainless steel in accordance with AIS 316.] [steel in accordance with ASTM A 36.  Ensure ASTM A 36 steel filter housings are powder coated and in accordance with American Architectural Manufacturers Association 2605 specifications.]  Drain filter housings must consist of a flat mounting plate flange to permanently mount the assembly to the existing structure shown on the plans in accordance with the size and shape of the weep hole.  If required for mounting purposes, ensure adapter plates are made of the same material as the drain filter housings.  Ensure drain filter housings consist of a perforated conical shell, extending into the existing structure a minimum of 3 inches, and providing a minimum of 30 square inches of perforated surface area.  Ensure perforations in the conical shell portion of the housing are at least 1/8 inch diameter, but not greater than 3/8 inch diameter, and account for greater than 50 percent of the conical shell surface area.  Ensure mounting hardware is stainless steel.

Provide a flexible and compressible gasket to ensure a watertight seal between the mounting plate and the existing structure.

Provide a rigid plastic cartridge type insert containing geotextile fabric that attaches to the steel drain filter flange and is removable to allow for periodic inspection and maintenance.  Ensure the cartridge is flame retardant and ultraviolet (U/V) resistant.  Provide woven geotextile fabric in accordance with section 910 of the Standard Specifications for Construction except as modified in the table below.

Table 1:  Geotextile Physical Requirements

| Mechanical Properties | Test Method | Unit | Minimum Average Roll Value |
| --- | --- | --- | --- |
| Permittivity (minimum – maximum) | ASTM D4491 | sec-1 | 0.25 - 1.5 |
| Apparent Opening Size (maximum) | ASTM D4751 | mm | 0.212 |

[Ensure the removable geotextile fabric cartridge includes a one-way check valve to prevent water and debris from entering the filter.  Protect the one-way check valve by a cover.] [Ensure the removable geotextile fabric cartridge is open ended.]

[Provide stone backfill material that is Coarse Aggregate Class 6A in accordance with section 902 of the Standard Specifications for Construction.]

Submit a General Certification to the Engineer for acceptance of the above materials.  Ensure the General Certification is accompanied by the product data sheets for all materials associated with the weep hole maintainable drain filter.  Visually inspect all materials prior to installation to ensure they are free from defects.  General Certification and Visual Inspection basis of acceptance are as defined in the Materials Quality Assurance Procedures Manual.

c.	Construction.  Core drill the (2½ inch)(4 inch)(6 inch) diameter weep hole(s) in the existing (INSERT PROJECT SPECIFIC STRUCTURE SUCH AS RETAINING WALL, ABUTMENT WALL, SHEET PILE WALL, etc.) at the locations and to the thickness shown on the plans.  Ensure the weep hole is flushed with water to remove any dust or debris prior to installing the drain filter.  Minimize the amount of soil loss during construction.

Install the drain filter flange flush with the existing structure.  Orient the drain filter in accordance with the manufacturer’s recommendations.  [Mount the drain filter using stainless steel screws with washers appropriate for the material of the existing structure.  Utilize the drain filter housing flange as a template for drilling holes.]  [Weld the drain filter to the existing steel structure with (INSERT DESIRED WELD SIZE AND LENGTH).]

d.	Measurement and Payment.  The completed work, as described, will be measured and paid for at the contract unit price using the following pay item:

Pay Item	Pay Unit

Maintainable Drain, Steel, __ inch	Each

Maintainable Drain, Steel, __ inch includes all labor, equipment and materials necessary to complete the work as described.